## Slide 1: Selective precipitation of potassium in seawater samples for improving the sensitivity of plain γ-ray spectrometry
Marco Ferrante,Matthias Laubenstein
Stefano Nisi, Francesco De Angelis

## Slide 2: The Gran Sasso National Laboratory
1400 m rock coverage
Muon flux reduction factor: 106

## Slide 3
In STELLA a lot of different samples with radiometric method and high sensitivity are measured.
To select the material for the underground experiments
To do measurements of scientific interest
  STELLA = SubTErranean Low Level Assay
12 HPGe detectors
4 silicon alpha detectors.
2 liquid scintillation counters (ultra low background)
7 active gas radon detectors

## Slide 4: Research goal
The goal of this work was the identification of a chemical method for the removal of K from sea water samples. Analytical techniques such as ICP-MS and AAS were used to check the efficiency.
The γ-spectroscopy measurements of some radionuclides, such as Th, U, Cs, Pb, Co, Ra and I in seawater samples with low levels of concentration, is very difficult for the high concentration of potassium in the matrix. Its Compton continuum makes the identification of the elements of interest rather difficult.

## Slide 5: ICP-MS
Sample
Introduction
Atomization and Ionization
Analisis and
Detection

## Slide 6: Atomic Absorption Spectometry (AAS)
Quantitative and qualitative analysis;
No strong dilution;

## Slide 7: Experimental Research
 | K removal %
Toluene | 27,9
Chloroform | 24,3
Benzene | 24,9
Step 1
AAS quantitative analysis.
Unsatisfactory results for our purposes.
Crown ethers are expensive.
18-Crown-6 (1,4,7,10,13,16-hexaoxacyclooctadecane) liquid-liquid extraction technique (Toluene, Chloroform,Benzene)
Simulate samples (KMnO4) and small volumes (50 mL)
Evaluate the real selectivity of Crown Ether for K.

## Slide 8: Experimental Research
Sodium Tetraphenylborate Technique
Developed by Witting (1950), Raff and Brotz (1951) actually is often use with seawater samples
[B(C6H5)4]- + K+ → K[B(C6H5)4]↓
The solubility of precipitate is lower between pH 4 and 6;
Kps~ 2.3 x 10-8 (20 °C);
Co-precipitation of Calcium e Magnesium is minimized with Na2CO3 glacial acetic acid;
Rb+, Cs+, NH4+, Hg+, Ag+, Tl+ form stable precipitates
Step 2

## Slide 9: Experimental work
1L Seawater Sample
3.42 g Sodium Tetraphenylborate and 0,5 g of Al2O3 dissolved in 100 mL of Milli-q water and Glacial Acetic Acid
100 mL of Na2CO3 5% solution
Filtered seawater
Filter 0,4 µm
Stirring
Seawater
+
Na2CO3
Filter 0,4 µm
PET bottle conditioned with HNO3 10% UP
Stirring

## Slide 10
Method validation:
            Selectivity
            Reproducibility
            Efficency
Analysis by AAS
Chart: ppm
| 64.994000000000227 | 579.51400000000001 | 921.52300000000002 | 2172.578 | 5492.6080000000002 | 8814.5130000000008 | 20454.27
 | 0 | 0.0252 | 0.0419 | 0.1031 | 0.2654 | 0.4279 | 0.997
Calibration with 6 potassium standards
    0.5 ppm
    1 ppm
    2 ppm
    5 ppm
    10 ppm
    20 ppm
 | Seawater | Seawater+tetraphenylborate
 | K (ppm) | K (ppm)
 | 516 | 35.5
 | 519 | 34.7
 | 525 | 35
Average | 520 | 35.1
93.25 %
Experimental work

## Slide 11: Method Validation
Selectivity
We spiked the samples with10 ppm of I and 20 ppb of U,Th,Cs,Co,Pb.
The analysis is made by quantitative ICP-MS.
volatile compounds
(Iodine,hydrogen iodide)
The selectivity of Tetraphenylborate for Cesium is described in literature.
Quantum mechanical calculations made with Gaussian03 and GaussView 3.07

## Slide 12: Method Validation
HF/631G | K+ | Na+ | [B(C6H5)4]- | K[B(C6H5)4] | Na[B(C6H5)4]
Hartree | -598.971672 | -161.659276 | -944.892377 | -1544.02115 | -1106.73756
Kcal/mole | -355854.7242 | -101441.1957 | -592919.9666 | -968873.2716 | -694477.8189
[B(C6H5)4]- + Na+ → Na[B(C6H5)4]↓
ΔG =-0.19 Hartree or -119.225 Kcal/mol;
[B(C6H5)4]- + K+ → K[B(C6H5)4]↓
ΔG =-0.43 Hartree or -269.825 Kcal/mol
HF/SDD | Na+ | Cs+ | [B(C6H5)4]- | Na[B(C6H5)4] | Cs[B(C6H5)4]
Hartree | -161.65927 | -19.72641 | -944.97283 | -1106.73756 | -964.82874
Kcal/mole | -101441.1919 | -12378.32228 | -592970.4508 | -694477.8227 | -605430.0344
[B(C6H5)4]- + Na+ → Na[B(C6H5)4]↓
ΔG = -0,11 Hartree or -69,025 Kcal/mol;
[B(C6H5)4]- + Cs+ → Cs[B(C6H5)4]↓
ΔG =-0,13 Hartree or -81,575 Kcal/mol
Quantum Mechanical Calculations
Selectivity

## Slide 13: Method Validation
Repeatability
The process was applied to three aliquots of a water sample and the process was repeated after one week and after 4 weeks.
 | Day 0 |  | After a week |  | After 4 weeks | 
 | K[ppm] | % K | K[ppm] | % K | K[ppm] | % K
H2O Seawater | 412±41 |  | 416±42 |  | 360±36 | 
H2O+TFB Rep 1 | 2.2±0.2 | 99.4 | 2.8±0.3 | 99.3 | 13.2±1.3 | 96.3
H2O+TFB Rep 2 | 5.4±0.5 | 98.7 | 8.3±0.8 | 98.0 | 8.8±0.8 | 97.6
H2O+TFB Rep 3 | 2.5±0.2 | 99.4 | 3.4±0.3 | 99.2 | 8.2±0.8 | 97.7
The method is repeatable

## Slide 14
Efficiency
To verify the method efficency, a synthetic sample of seawater was prepared and processed with the tetraphenylborate method. The results are compared with the real sample.
 | K [ppm] | % K precipitated
Seawater | 412±41 | 
Synthetic Seawater | 492±49 | 
H2O +TFB Rep 1 | 2.2±0.2 | 99.4
H2O +TFB Rep 2 | 5.4±0.5 | 98.6
H2O +TFB Rep 3 | 2.5±0.2 | 99.4
SyH2O+TFB Rep 1 | 8.6±0.8 | 98.2
SyH2O+TFB Rep 2 | 6.5±0.6 | 98.7
SyH2O+TFB Rep 3 | 3.4±0.3 | 99.3
The results are comparable
Method Validation

## Slide 15
Reagent stability test.
 | Day 0 |  | After a week |  | After 4 weeks | 
 | [ppm] | % K | [ppm] | % K | [ppm] | % K
H2O seawater | 412±41 |  | 416±42 |  | 360±36 | 
Synthetic seawater | 492±49 |  | 449±45 |  | 492±49 | 
H2O +TFB Repl 1 | 2.2±0.2 | 99.4 | 2.9±0.3 | 99.3 | 13.2±1.3 | 96,3
H2O +TFB Rep 2 | 5.4±0.5 | 98.7 | 8.3±0.8 | 98.0 | 8.8±0.8 | 97,6
H2O +TFB Rep 3 | 2.5±0.2 | 99.4 | 3.4±0.3 | 99.2 | 8.2±0.8 | 97,7
syH2O +TFB Rep 1 | 8.6±0.8 | 98.2 | 8.3±0.8 | 98.1 | 8.2±0.8 | 98,3
syH2O +TFB Rep 2 | 6.5±0.6 | 98.7 | 3.4±0.3 | 99.8 | 8.3±0.8 | 98,3
syH2O +TFB Rep 3 | 3.4±0.3 | 99.3 | 4.6±0.4 | 99.0 | 8.6±0.8 | 98,2
Method Validation
Efficiency

## Slide 16
Blank test
To prevent the possibility of contamination by the various reagents and instruments used during the procedure of precipitation (beakers, flasks, Milli-Q water, Na2CO3, Acetic Acid, etc. ..) we performed some blank tests.
Element | Conc. | Blank test 1 | Blank test 2
Co | [ppb] | <0.3 | <0.3
I | [ppm] | <0.5 | <0.5
Cs | [ppb] | <0.5 | <0.5
Pb | [ppb] | <0.5 | <0.5
Th | [ppb] | <0.5 | <0.5
U | [ppb] | <0.5 | <0.5
There is no external contamination
Method Validation

## Slide 17: Sample preparation and analysis
Samples for γ-spectroscopy measument were prepared.
Potassium removal efficiency was checked by ICP-MS quantitative analysis.
 | K[ppm] | % K
Seawater | 460±50 | 
H2O +TFB | 0.98±0.09 | 99.8
 | K[ppm] | % K
Seawater | 330±30 | 
H2O +TFB | 25±3 | 92.4
 | K[ppm] | % K
Seawater | 360±40 | 
H2O +TFB | 13±1 | 96.3
Average |  | 96.6
Sample 1
Sample 2
Sample 3

## Slide 18: Gamma spectroscopy measurement
STELLA (SubTerranean Low Level Assay)
Sample 1 measured in polystyrene box
Samples 2 and 3 measured in polypropylene box (Marinelli)
Samples in contact with detector
High Efficency

## Slide 19: Gamma spectroscopy measurement
Detector | Sample | Rate [d-1 g-1] Before | Rate [d-1 g-1] After | reduction factor
GeCris | 1 | 2.820 ± 0.020 | 0.0230 ± 0.0015 | 0.9920 ± 0.0060
GeMi | 2 | 1.570 ± 0.010 | 0.112 ± 0.001 | 0.9290 ± 0.0120
GeMi | 3 | 1.570 ± 0.010 | 0.0350 ± 0.0012 | 0.9780 ± 0.0350
40K
Energy ~ 1460.8 keV
Reduction factor 120.5
Reduction factor 13.9
Reduction factor 44.6

## Slide 20: Radionuclides measurement
Standard deviation depends on:
Density of sample
Composition
Geometry of detector
Detector | Sample | Rate [d-1 g-1] Before | Rate [d-1 g-1] After | reduction factor
GeCris | 1 | 0.0170± 0.0020 | 0.0020 ± 0.007 | 0.87 ± 0.31
GeMi | 2 | 0.0090 ± 0.0010 | 0.0020 ± 0.004 | 0.81 ± 0.19
GeMi | 3 | 0.0090 ± 0.0010 | 0.0020 ± 0.004 | 0.86 ± 0.20
Detector | Sample | Rate [d-1 g-1] Before | Rate [d-1 g-1] After | reduction factor
GeCris | 1 | 0.0150 ± 0.0025 | 0.0030 ± 0.010 | 0.79 ± 0.33
GeMi | 2 | 0.0090 ± 0.0012 | 0.0030 ± 0.005 | 0.70 ± 0.16
GeMi | 3 | 0.0090 ± 0.0012 | 0.0020 ± 0.005 | 0.77 ± 0.22
Determination of' 238U by
measuring 234mPa
Energy ~ 1001 keV
Determination of 228Ra by
Measuring 228Ac
Energy ~ 911 keV
Detector | Sample | Rate [d-1 g-1] Before | Rate [d-1 g-1] After | reduction factor
GeCris | 1 | 0.0330 ± 0.0020 | 0.0130 ± 0.005 | 0.61 ± 0.05
GeMi | 2 | 0.0200 ± 0.0010 | 0.0070 ± 0.003 | 0.66 ± 0.04
GeMi | 3 | 0.0200 ± 0.0010 | 0.0060 ± 0.002 | 0.71 ± 0.05
Direct determination of
226Ra
Energy ~ 186 keV
Detector | Sample | Rate [d-1 g-1] Before | Rate [d-1 g-1] After | reduction factor
GeCris | 1 | 0.0190 ± 0.0023 | 0.0030 ± 0.009 | 0.85 ± 0.29
GeMi | 2 | 0.0120 ± 0.0011 | 0.0020 ± 0.003 | 0.81± 0.14
GeMi | 3 | 0.0120 ± 0.0011 | 0.0010 ± 0.003 | 0.87 ± 0.17
Direct determination of
60Co
Energy ~ 1173 keV
& 1332 keV

## Slide 21: Gamma spectroscopy measurement
Measurement Problems
Cs+
Co-precipitation with K+;
I-
Is volatile;
232Th
Is sparingly soluble in water;
210Pb
The emitted photon energy is low and the probability of emission is low;

## Slide 22: Conclusions
This work has shown that the selective precipitation of potassium with sodium tetraphenylborate is leading to an increase of sensitivity of radionuclides such as 238U,226Ra, 228Ra, 60Co in γ-ray spectrometric analysis.
Improve by almost one order of magnitude
Reduction of 40K

## Slide 23: Conclusions
Comparison between γ-ray spectroscopy and ICP-MS measurement
Sample | Technique | % K
1 | γ-ray spectroscopy | 99.2
 | ICP-MS | 99.8
2 | γ-ray spectroscopy | 92.9
 | ICP-MS | 92.4
3 | γ-ray spectroscopy | 97.8
 | ICP-MS | 96.3

## Slide 24: Conclusions
    Eliminate high percentages of Potassium is rather inexpensive;
    Improvement of sensitivity for radionuclides;
    Compare ICP-MS and γ -ray spectroscopy;
Future development:
    Investigation of the possibility to apply this method to different kind of matrices;
    Recovery of reagents for a further reduction of the costs;

## Slide 25: Acknowledgements
Prof. Francesco De Angelis
Ing. Stefano Nisi
Dr. Matthias Laubenstein

## Slide 26: Thank you for your attention !