## Slide 1: Radon and its Progeny A Pervasive Problem for Low Background Counting (with Lessons from Borexino and Biology)
Frank Calaprice
Princeton University

## Slide 2: Solar Neutrinos with Borexino Milestones in Low-Background Counting
  ✓ 7Be 46.0 cpd/100t ± 5%. PRL 2011
  8B (> 3 MeV) 0.22 cpd/100t ± 19% PRD 2010
  pep 3.1 cpd/100t ± 22% PRL 2012
  pp 144 cpd/100t ± 16% Nature 2014
  Direct Measurement of Neutrinos in pp-chain
  CNO limit: < 7.9 cpd/100t PRL 2012
  ?? CNO Low/Hi metallicity: 3 - 5 cpd/100t Underway…

## Slide 3: Solar Neutrino Spectra
Neutrino Energy Spectrum
Neutrino-Electron Elastic Scattering Energy Spectrum
X2 for keV

## Slide 4: Overview of the Borexino Detector (Lots of Active Shielding)
Shielding against external
backgrounds is very good.
  Water: 2.25m
  Buffer zones: 2.5 m
  Outer scintillator zone: 1.25 m
Main backgrounds are in Liquid Scintillator.
  14C/12C , 11C (cosmogenic)
  U, Th decay chain.
  222Rn progeny (210Pb, 210Bi, 210Po)
  85Kr
Pulse shape discrimination.
  Alpha-beta separation is important

## Slide 5: The 210Po- 210Pb(210Bi) Mystery
2210Po: ~8000 cpd/100t
2210Bi+CNO: ~15 cpd/100t
210Bi: ~10 CPD/100t]

## Slide 6: The 238U and 232Th Decay Chains
Radon deposits 210Pb (22 yr) which later contaminates scintillator with 210Bi (1 MeV b) and 210Po (5 MeV a).

## Slide 7: The 210Bi – 210Po Puzzle of 2007
If 210Bi and 210Po come from 210Pb in the scintillator, their rates should be similar.
The factor of ~800 difference was never understood.
New studies suggest a possible explanation that depends on radon progeny in water, and on biology.

## Slide 8: Low-Background Scintillator Strategy
Built nylon vessel in first low-radon cleanroom.
  Hermetically sealed class-100 cleanroom.
  Vacuum swing charcoal filter developed to remove radon from make-up air.
“Precision cleaning” methods developed
  Class-30 MIL-STD-1246C specification achieved for particulates in fluid handling system.
Developed scintillator purification systems
  Distillation, water extraction , and nitrogen stripping.

## Slide 9: Nylon Scintillator Containment Vessel Fabricated in special Princeton Low-Radon Cleanroom
John Bahcall
First hermetically sealed
cleanroom with low-radon
air was developed to avoid
surface radioactivity due
to 222Rn daughters:
 210Pb (22 yr).
Fabrication time: > 1 yr
Low-radon cleanrooms
are now more common in
low-background research.

## Slide 10: Purification of PPO-PC Master Solution
Water Extraction (not shown)
  PPO-PC solution mixed with de-ionized water.
  Scintillator and water separate.
Distillation of PPO-PC.
  Falling film evaporator
  N2 stripping
Distillation and N2 stripping of PPO-PC
Water extraction was done to remove K in PPO.
New studies show it may have introduced 210Po.

## Slide 11: PC Distillation and N2 Stripping and in-line Mixing of PPO-PC. (2007)

## Slide 12: Initial Measurements (2007-2010)
Solar Neutrinos
  7Be, 8B, pep
Geo-neutrinos
  238U and 232Th anti-neutrinos
Search for Rare Processes
  Solar axions, Pauli exclusion principle.

## Slide 13: Re-Purification of Liquid Scintillator (2010-2011)
Reduce backgrounds by “loop”scintillator purification using:
  “water extraction” and “nitrogen stripping”
First measurement of pp neutrinos, 2014
  Enabled with lower 85Kr and 210Bi backgrounds.
Feasibility study for CNO neutrinos.
  More reduction of 210Bi needed.

## Slide 14: Loop Re-Purification of Liquid Scintillator
“Loop” purification is achieved by draining fluid from bottom of vessel, passing it through purification system, and returning to the top.
Processes available are:
  Water extraction or distillation
  Nitrogen stripping (85Kr)

## Slide 15: Water Extraction and Nitrogen Stripping Performed 2010-2011
High purity water mixed with scintillator extracts impurities from the scintillator.
  Water and scintillator separate.
  Scintillator stays intact.
LNGS groundwater is first purified by reverse osmosis and ion-exchange in water plant.
Single stage evaporator used to distill and re-use water in “water extraction plant”.
  10% of water is continuously wasted and replaced.
The water extraction system.
N2 stripping column used in series

## Slide 16: Results of 6 Cycles of Re-purification
Technical difficulties with 3 cycles; then 3 good cycles.
Impressive reductions of lower part of the 238U and 232Th chains.
  Bi-Po’s less than 1 count/100t/year.
85Kr reduced below detection limit.
210Bi (210Pb) modest reduction. Further reduction needed.
210Po not reduced.

## Slide 17: Studies of Radioactivity in Water
Poor removal of 210Po triggered studies of radioactivity in the water.
LNGS ground water was known to have 222Rn at 10,000 Bq/m3.
  New studies aimed at measuring Rn progeny: 210Pb (208Pb), 210Po.
Discovery #1- Nov 2012
  De-ionization is much less effective in removing 208Pb and 210Po from water compared to removing common impurities such as Mg.
Discovery #2 – April 2013 (Literature search by Brooke Russell)
  Biological processes in micro-organisms in groundwater produce a volatile dimethyl polonium.
  Dimethyl polonium has estimated boiling point of 138 C.
  Removal of 210Po from water, or from PPO-PC master solution, by single-stage distillation may not not be as effective as expected.

## Slide 18: Purification of LNGS Groundwater Deionization is less effective for Pb and Po than for Mg.
222Rn in groundwater: ~10,000 Bq/m3
Notes: This could explain a factor of ~100 between 201Pb and 210Po.
All that is needed is factor of 10 in biological background.

## Slide 19: Biological Methylation of Po (Where Physics meets Biology)
Methylation
  Enzymatic (catalytic) transfer of a methyl group from a donor atom to a receptor atom (e.g., 210Po).
Biological Methylation (Biomethylation)
  Methylation carried out by enzymes in biological systems, bacteria, fungi, etc.
  Well established, with vast literature for stable elements.
  Biomethylation occurs in chalcogens: O, S, Se, Te, Po.
Dimethyl polonium (CH3)2Po – Recent studies
  Produced by micro-organisms in ground water.
  Could be main form of Po in groundwater.
  Not easily removed; Estimated boiling point: 138 C.

## Slide 20: Test of Special Distillation to Remove Dimethyl-210Po from Water.
Small-scale fractional distillation system tested at Princeton to remove 210Po from groundwater.
  6-foot tall column with structured packing and high reflux designed for x1000 reduction of 138 C impurity.
  Princeton groundwater: x5 higher 210Po than LNGS
  210Po in water measured by auto-deposition on silver foils and alpha particle counting.
Successful Results:
  No 210Po detected in product: reduction factor > 300.

## Slide 21: Upgrade of Water Extraction System Previous & New Upgrade with 2 New Fractional Distillation Columns
Make-up water
system not shown.
Proposed
System
Present
System
Make-up water
system not shown.
Proposed
System
Current
System

## Slide 22: Conclusions
Poor removal of 210Pb and 210Po in water purification process and bio-methylation of 210Po have been identified as serious sources of background.
  Can explain initial much higher 210Po >> 210Bi.
  New distillation methods to improve water extraction have been identified and tested. Columns under construction.
Direct distillation of PC and PPO is also available.
  Existing distillation column for PC
  A new distillation column for PPO
Radioactivity in “purified groundwater” is problematic.
  Use with care in other low-background experiments.
Prospects for CNO with Borexino look good.

## Slide 23: The End

## Slide 24: Spares

## Slide 25: Element Biomethylation
John Thayer,
“Biological methylation of
less-studied elements.”
Applied Organometallic Chem.,
16, 677 (2002)
1: bacteria
2: fungi/algae/yeast
3: plants
4: animals

## Slide 26: N2 Stripping of 210Po from Well Water

## Slide 27: Volatility of 210Po Spiked Bread Mold

## Slide 28: 210Pb and 210Po in the Environment
Radon in Outside Air (Bq/m3)
222Rn: ~10
210Pb: 0.12 – 1.5
210Po: 0.03 – 0.30
Radon progeny in Groundwater. Highly variable, depending on rock.
210Pb (Bq/m3) 210Po (Bq/m3)
1. Italian mineral water: 0.04 - 21
2. Finnish wells: 7-40 13 - 48
3. California wells: 3.7 -1400 0.25-550
4. Calif. health limits: 37 26
EU health limits: 200 100
Ref: Persson and Holm, J. Environ. Radioactivity, 102, 420 (2011)